## Slide 1: Jaringan Wireless Area Network (WLAN) IEEE 802.11
Soleh Elfrianto Hardiyono
PENS D4 LJ PJJ 2014
2110147044
KTI [Tugas 3]

## Slide 2: WLAN IEEE802.11 adalah …
Serangkaian spesifikasi kendali akses medium dan lapisan fisik untuk mengimplementasikan komunikasi komputer wireless local area network di frekuensi 2.4, 3.6, 5, dan 60 GHz. Mereka diciptakan dan dioperasikan oleh Institute of Electrical and Electronics Engineers. Versi dasar dirilis tahun 1997 dan telah melalui serangkaian pembaruan dan menyediakan dasar bagi produk jaringan nirkabel Wi-Fi.

## Slide 3: Perbedaan LAN dan WLAN
WLAN memakai gelombang radio sebagai physical layer-nya.
WLAN menggunakan MAC CSMA/CA (Carrier Sense Multiple Access Collision Avoidance) sedangkan LAN menggunakan CSMA/CD (Carrier Sense Multiple Access Collision Detection).
WLAN mendukung pengguna yang bersifat mobile, sedangkan LAN tidak

## Slide 4: Kode tertentu untuk standarisasi dalam teknologi komunikasi WLAN IEE 802.11 :
802.1: LAN/MAN Management and Media Access Control Bridges
802.2: Logical Link Control (LLC)
802.3: CSMA/CD (Standar untuk Ehernet Coaxial atau UTP)
802.4: Token Bus
802.5: Token Ring (bisa menggunakan kabel STP)
802.6: Distributed Queue Dual Bus (DQDB) MAN
802.7: Broadband LAN
802.8: Fiber Optic LAN & MAN (Standar FDDI)
802.9: Integrated Services LAN Interface (standar ISDN)

## Slide 5: Cont’..
802.10: LAN/MAN Security (untuk VPN)
802.11: Wireless LAN (Wi-Fi)
802.12: Demand Priority Access Method
802.15: Wireless PAN (Personal Area Network) > IrDA dan Bluetooth
802.16: Broadband Wireless Access (standar untuk WiMAX)

## Slide 6: Standarisasi IEEE 802.11a
Standard IEEE 802.11a bekerja pada frekuensi 5GHz mengikuti standard dari UNII (Unlicensed National Information Infrastructure). Teknologi IEEE 802.11a tidak menggunakan teknologi spread-spectrum melainkan menggunakan standar frequency division multiplexing (FDM). Mampu mentransfer data hingga 54 Mbps

## Slide 7: Standarisasi IEEE 802.11b
Standar 802.11b saat ini yang paling banyak digunakan satu. Menawarkan thoroughput maksimum dari 11 Mbps (6 Mbps dalam praktek) dan jangkauan hingga 300 meter di lingkungan terbuka. Ia menggunakan rentang frekuensi 2,4 GHz, dengan 3 saluran radio yang tersedia. Transmisi data 5,4 hingga 11 Mbps

## Slide 8: Standarisasi IEEE 802.11c
Standar 802.11c (disebut WiFi), yang menjembatani standar 802.11c tidak menarik bagi masyarakat umum. Hanya merupakan versi diubah 802.1d standar yang memungkinkan 802.1d jembatan dengan 802.11-perangkat yang kompatibel (pada tingkat data link).

## Slide 9: Standarisasi IEEE 802.11e
Standar 802.11e yang dimaksudkan untuk meningkatkan kualitas layanan pada tingkat data link layer. Tujuan standar ini adalah untuk menentukan persyaratan paket yang berbeda dalam hal bandwidth dan keterlambatan transmisi sehingga memungkinkan transmisi yang lebih baik suara dan video.

## Slide 10: Standarisasi IEEE 802.11f
Standar 802.11f adalah rekomendasi untuk jalur akses vendor produk yang memungkinkan untuk menjadi lebih kompatibel. Ia menggunakan Inter-Access Point Protocol Roaming, yang memungkinkan pengguna roaming transparan akses beralih dari satu titik ke titik lain sambil bergerak, tidak peduli apa merek jalur akses yang digunakan pada infrastruktur jaringan. Kemampuan ini juga hanya disebut roaming.

## Slide 11: Standarisasi IEEE 802.11g
Standar 802.11g menawarkan bandwidth yang tinggi (54 Mbps throughput maksimum, 30 Mbps dalam praktek) pada rentang frekuensi 2,4 GHz. Standar 802.11g mundur-kompatibel dengan standar 802.11b, yang berarti bahwa perangkat yang mendukung standar 802.11g juga dapat bekerja dengan 802.11b.

## Slide 12: perangkat WLAN yang dapat digunakan pada tipe yang berbeda dalam struktur jaringan :
  Station
  Access Point
  Wireless Routers
  Wireless bridges

## Slide 13: infraStruktur WLAN

## Slide 14: WLAN Station
Menggunakan standar 802.11 pada MAC dan physical layer untuk mendukung komunikasi nirkabel, contoh :
notebook,
komputer meja (PC),
peralatan yang menggunakan access point, bridge dan router

## Slide 15: IEEE 802.11 Physical Layer: Spread Spectrum
Frequency Hopping Spread Spectrum (FHSS)
  The FHSS physical layer has 22 hop patterns to choose from. The frequency hop physical layer is required to hop across the 2.4GHz ISM band covering 79 channels. Each channel occupies 1Mhz of bandwidth and must hop at the minimum rate specified by the regulatory bodies of the intended country. A minimum hop rate of 2.5 hops per second is specified for the United States.
Direct Sequence Spread Spectrum (DSSS)
  The DSSS physical layer uses an 11-bit Barker Sequence to spread the data before it is transmitted. Each bit transmitted is modulated by the 11-bit sequence. This process spreads the RF energy across a wider bandwidth than would be required to transmit the raw data. The processing gain of the system is defined as 10x the log of the ratio of spreading rate (also know as the chip rate) to the data. The receiver despreads the RF input to recover the original data.

## Slide 16: NIC (Network Interface Card)
Kemampuan WLAN pada PC dan notebook yaitu menggunakan NIC dan driver. NIC didesain supaya dapat digunakan pada laptop atau notebook yang memiliki slot PCI card
Kartu Adapter Nirkabel SMC Networks 802.11a.

## Slide 17
40
IEEE 802.11 Physical Layer： Frame format
Control
Duration
Addr1
Addr2
Addr3
Addr4
Control
Data
CRC
Distribution System
AP1
AP2
AP3
A
B
C
D
E
F
Frame Type (RTS,CTS,…)
ToDS
FromDS
Ultimate
Destination (E)
Immediate
Sender (AP3)
Intermediate
Destination
(AP1)
Source
(A)
RTS: Request-to-Send
CTS: Clear-to-Send

## Slide 18
41
IEEE 802.11 Physical Layer： Frame format (con’t)
Header：30Bytes including control
information、addressing、sequence
number、duration
Data ：0~2312Bytes,changing with frame
type
Error control：4Bytes,with CRC32
Frame control | Duration /ID | Addressing 1 | Addressing 2 | Addressing 3 | Sequence control | Addressing 4 | Frame body | CRC

## Slide 19
42
IEEE 802.11 Frame format (con’t)
Protocol version | Type | Subtype | To DS | From DS | More flag | Retry | Pwr mgt | More Data | WEP | Order
Frame control | Duration /ID | Addressing 1 | Addressing 2 | Addressing 3 | Sequence control | Addressing 4 | Frame body | CRC

## Slide 20: MAC Layer：CSMA/CA
43
802.11 Collision Resolution
CSMA/CA
Hidden Terminal effect
How it works?
Carrier Sense Multiple Access/Collision Avoidance

## Slide 21
44
802.11 Collision Resolution
Two senders might send RTS at the same time
Collision will occur corrupting the data
No CTS will follow
Senders will time-out waiting for CTS and retry with exponential backoff
RTS: Request-to-Send
CTS: Clear-to-Send

## Slide 22: 802.11 transmission Protocol
45
Sender A sends Request-to-Send (RTS)
Receiver B sends Clear-to-Send (CTS)
  Nodes who hear CTS cannot transmit concurrently with A (red region)
  Nodes who hear RTS but not CTS can transmit (green region)
Sender A sends data frame
Receiver B sends ACK
Nodes who hear the ACK can
now transmit
RTS
CTS
A
B

## Slide 23
46
Hidden Terminal effect
(a) A and C cannot hear each other because of obstacles or signal attenuation; so, their packets collide at B
(b) goal: avoid collisions at B
CSMA/CA: CSMA with Collision Avoidance

## Slide 24: CSMA/CA (Collision Avoidance)
47
sense channel idle for DISF sec (Distributed Inter Frame Space), send RTS
receiver returns CTS after SIFS (Short Inter Frame Space)
CTS “freezes” stations within range of receiver (but possibly hidden from transmitter); this prevents collisions by hidden station during data
transmit data frame (no Collision Detection)
receiver returns ACK after SIFS (Short Inter Frame Space)
- if channel sensed busy then binary backoff
NAV: Network Allocation
Vector (min time of deferral)
(= min packet size in 802.3)
RTS and CTS are very short: collisions during data phase are thus very unlikely (the end result is similar to Collision Detection)

## Slide 25
48
802.11b security features
ESSID
  Network name, not encrypted
  Rudimentary because the ESS ID is broadcast in beacon frames
Association
  Capability to register a station with a WLAN
WEP (Wired Equivalent Privacy)
  encrypts data using RC4 with 40 to 128-bit shared keys
  Some vendors do in software, others in hardware
  Symmetric Scheme – Same Key For Encrypt/Decrypt
  Intended For:
    Access Control (no WEP key, no access)
    Privacy (encrypt data stream)

## Slide 26: Wired Equivalent Privacy
49
Why Wired Equivalence Privacy?
  Wireless medium has no packet boundaries
    WEP control access to LAN via authentication
  Wireless is an open medium
    Provides link-level security equivalent to a closed medium (note: no end-to-end privacy)
Two Types of Authentication
  Set on Client/Access Points (Same)
  Open (Default): Clear-Text Authentication
    No WEP key required for access
  Shared-Key: Clear-Text Challenge (by AP)
    Must respond with the correct WEP key, or no access
Broken due to bad use of the cipher [Walker, Berkeley Team, Arbaugh, Fluhrer]

## Slide 27
50
WEP (cont.)
RSA “Fast-Packet Keying”
  Fix Approved By IEEE Committee (2001)
  Generates Unique Encryption Keys For Data Packets
  Reduces Similarities Between Successive Packets
Temporal Key Integrity Protocol (TKIP)
  Approved 2002/01/25, Optional 802.11 Standard
  Helps Defeat Passive Packet Snooping
  Dynamic Keys Defeat Capture of Passive Keys (WEP Hole)
  Some Vendors Starting to Incorporate

## Slide 28: Auth: Captive portal
51
Synopsis:
  Intercepts first HTTP connection
  Redirect to authentication page using SSL
  Does access control based on login / password
Products
  NoCatAuth (freeware)
  Vernier Networks (commercial)
  E-Passport, EZone
Costs:
  Not intrusive nor expensive

## Slide 29
52
Auth: 802.1X
Synopsis:
  authentication before giving access to the network
  Requires a PKI certificate on each client
  Requires a central RADIUS server with EAP
Products:
  CISCO Aironet 350 Series
  Microsoft Windows XP
Costs:
  Deployment is intrusive
  Maintenance is expensive
  Can be a corporate wide solution

## Slide 30: Extensible Authentication Protocol (EAP [RFC 2284])
53
A port begins in an unauthorized state, which allows EAP traffic only.
Once the Authenticator has received a Supplicant’s request to connect (an EAPOL-Start), the Authenticator replies with an EAP Request Identity message.
The returning Response Identity message is delivered to the Authentication Server.

## Slide 31: #Tag
wikipedia
PowerPoint
wikipedia
Images
Microsoft
yahoo
excel
office
Chart
Retro-style
chart
Workflow
windows
google
Metro ui
Icons
word
business
bing
Blue
Grey
graph